## Slide 2: Industrial Wireless Networks
Services and Innovation for Industry 4.0 (SII40)
Xenofon (Fontas) Fafoutis Associate Professor xefa@dtu.dk
www.compute.dtu.dk/~xefa
20/7/2024
This lecture is licensed under CC BY 4.0

## Slide 3: whoami
Associate Professor at DTU Compute
  Section for Embedded Systems Engineering
  https://www.compute.dtu.dk/sections/ese
Visiting Professor at UNIPR
Research Interests
  Wireless Embedded Systems
  Industrial Wireless Networks
  Embedded AI
  (Industrial) Internet of Things
More info: http://xefa.eu
Embedded Systems Engineering section October 2023

## Slide 4: Lecture Outline
Introduction to Industrial Wireless Networks
Introduction to IEEE 802.15.4 TSCH
Time Synchronisation: Communication based on a randezvous
TSCH Mechanics: Time Slotting and Channel Hopping
TSCH Mechanics: Scheduling
TSCH Mechanics: Joining a TSCH Network

## Slide 5: Requirements of (Industrial) Networked Embedded Systems
Scalability
  Supported number of embedded systems
Throughput
  Bytes received per second
Reliability (Packet Delivery Ratio, PDR)
  Number of packets received over packets sent
Latency/Delay
  Time interval from the time a packet is sent to the time packet received
Jitter
  Variability of latency/delay
Time-sensitivity or determinism
  Predictable/bounded latency and jitter
Energy Efficiency and Consumption
  All above need energy

## Slide 6: Requirements of (Industrial) Networked Embedded Systems
Scalability
  Supported number of embedded systems
Throughput
  Bytes received per second
Reliability (Packet Delivery Ratio, PDR)
  Number of packets received over packets sent
Latency/Delay
  Time interval from the time a packet is sent to the time packet received
Jitter
  Variability of latency/delay
Time-sensitivity or determinism
  Predictable/bounded latency and jitter
Energy Efficiency and Consumption
  All above need energy
Trade-offs: There is no solution that optimises all; we need figure out what we can afford to sacrifice

## Slide 7: Industrial Embedded Networks
Industrial Networks carry vital and often safety critical data
  Tend to prioritise reliability and determinism over throughput and energy efficiency
  Best-effort data may co-exist (e.g. vehicle sensor data vs entertainment)
Common features
  Schedule-based communication (avoid contention-based protocols)
  Time synchronisation
  Traffic prioritisation
  Redundancy
  Interference mitigation
Examples
  TSCH
  TSN

## Slide 8: Industrial Wireless Networks
The 6TiSCH protocol stack
A collection of IEEE/IETF standards
Aiming at industrial wireless networks that require high reliability and deterministic delay/jitter
Main components
  RPL
  IPv6
  6top
  IEEE 802.15.4 TSCH
IEEE 802.15.4
IEEE 802.15.4e TSCH
6top
6LoWPAN
IPv6
TCP / UDP / ICMP
MQTT / CoAP / others
IEEE
IETF
6TiSCH: https://doi.org/10.1007/978-3-319-04223-7_5

## Slide 9: IEEE 802.15.4 PHY
A low-power wireless standard for Low-Rate Wireless Personal Area Networks (LR-WPANs)
  Supports two ISM Bands (2.4 GHz, sub-GHz)
  250 kbps data rate @ 2.4 GHz
  127-byte packets
  16 channels @ 2.4 GHz (+ 1 channel @ 868 MHz in Europe)
  Supports encryption/authentication
Used in smart home/city/* wireless networks (Thread, Zigbee)
Used in industrial wireless networks (6TiSCH)
2405
2425
2445
2465
2410
2430
2450
2470
2415
2435
2455
2475
2420
2440
2460
2480
Frequency (MHz)
IEEE 802.15.4
BLE
WiFi (Ch 1,6,11)

## Slide 10: IEEE 802.15.4 MAC
Traditional IEEE 802.15.4-2011 MAC
  Based on two classes of devices (asymmetric resources)
  Full-Function Devices (FFD): Coordinator, frame forwarder
  Reduced-Function Devices (RFD): Simple, energy-preserving
  Supports contention-based (CSMA/CA) and contention-free (GTS) communication
IEEE 802.15.4e MAC Enhancements
  Enhanced MAC protocols for industrial applications
  DSME (Deterministic and Synchronous Multi-channel Extension)
  LLDN (Low Latency Deterministic Network)
  TSCH (Time Slotted Channel Hopping)

## Slide 11: IEEE 802.15.4 TSCH
TSCH (Time-Slotted, Channel Hopping)
  A MAC protocol based on the IEEE 802.15.4 PHY
TSCH supports
  Multi-hop networks (line, tree, mesh) topologies
  Radio duty cycling in all devices
TSCH provides
  Very high reliability (99.99%+ PDR)
  Interference avoidance
  Predictable delay/jitter/energy consumption
  Time synchronisation (10ms)

## Slide 12: TSCH Features
A combination of TDMA and FDMA
Time-Slotted: Synchronous schedule-based channel access
  Predictable channel access, possible to eliminate collisions
Channel Hopping: Use of multiple frequency channel in a rotating fashion
  Resilience to external interference
TSCH traces its roots to older industrial wireless standards
  Time Synchronized Mesh Protocol (TSMP, 2006) by Dust Networks (proprietary)
  WirelessHART (2007) by the HART Communication Foundation
  ISA100.11a (2009) by the International Society of Automation (ISA)

## Slide 13: The Problem of Synchronous Communication
Devices agree on a rendezvous point in time to turn on their radios to exchange data
Example
  Dev 1 and Dev 2 agree to exchange data in 1 minute
  Dev 1 puts a timer for 1 minute, goes to sleep, when timer expires it starts transmitting
  Dev 2 puts a timer for 1 minute, goes to sleep, when timer expires it starts listening
  What will happen?

## Slide 14: The Problem of Synchronous Communication
Devices agree on a rendezvous point in time to turn on their radios to exchange data
Example
  Dev 1 and Dev 2 agree to exchange data in 1 minute
  Dev 1 puts a timer for 1 minute, goes to sleep, when timer expires it starts transmitting
  Dev 2 puts a timer for 1 minute, goes to sleep, when timer expires it starts listening
  If Dev 1 and Dev 2 have no relative drift, it will work OK
  If Dev 1’s clock faster, Dev 2 will miss the transmission
  If Dev 2’s clock faster, Dev 1 will miss the listening window

## Slide 15: Guard Time
The receiver puts the radio in listen mode a bit before the rendezvous point and keeps it on for a while after to account for both positive and negative drift
Trade-off
  Large guard time improves robustness to time sync error
  But it increases the idle listening (and occupies bandwidth)
Blue: transmit
Green: receive
Yellow: listen
Gray: sleep

## Slide 16: Implicit Synchronisation
Relative time synchronisation without explicit synchronisation frames (overhead)
Rendezvous-based MAC can have implicit synchronisation using the data frames
  Receiver expects the transmission at T1 but it happens at T2
  It can then calculate the offset as o = T2-T1
”Free” resynchronisation on each data transmission
  A data transmission must happen before the synchronisation error becomes larger than what the guard time can handle
Runtime drift compensation
  The drift is constant in the short term (assuming constant temperature)
  The receiver can learn the drift by diving the offset to the time passed since last synchronisation
Blue: transmit
Green: receive
Yellow: listen
Gray: sleep

## Slide 17: TSCH: Timeslots and Time Synchronisation
Network-wide Time Synchronisation
  All devices in a TSCH network are time synchronised with each other
  Relative time synchronisation based on the implicit synchronisation technique
Time is split into timeslots
  Each slot is long enough to support:
    Transmission of a frame of maximum size (~4 ms)
    An acknowledgement (~0.35 ms)
    The guard time (~2 ms)
    Time required to switch from TX to RX mode, encryption/decryption
  The duration of the timeslot is not imposed by the standard
    Typical timeslot size is 10 ms
    Some older radios are slow at switching from TX to RX mode and need 15ms

## Slide 18: TSCH: Timeslot
A timeslot defines a transmission opportunity
  An actual frame transmission may not happen if there is nothing to transmit!
The sender initiates the frame transmission at TxOffset after the beginning of the timeslot
The receiver listens to the channel for the time defined by the Guard Time (G)
  The guard time is equally spaced around the expected transmission time to account for both positive and negative drift
  If a preamble is captured within the guard time, the receiver stays on to capture the full frame
  Otherwise, the receiver goes to sleep
After a frame transmission, sender and receiver swap the modes of their radios for the ACK
Tx Data
Tx ACK
Rx ACK
Rx Data
G
G
TxOffset
Timeslot Length
Tx
Rx

## Slide 19: TSCH: Guard Time
The guard time allows for a certain degree of synchronisation error
  Periodic synchronisation is required
Longer Guard Time
  More robust to synchronisation errors
  Less frequent synchronisation required
  More idle listening, more energy consumption
  Occupy the channel, bigger slots
  Fewer slots per second, less data
Ideally as short as possible, but long enough to maintain robust synchronisation
Example
  10 ppm drift, 2.2ms guard → sync. every ~100 seconds
  10 ppm drift, 0.2ms guard → sync. every ~2 seconds
Time Sync in TSCH: https://doi.org/10.1109/LCN.2016.042

## Slide 20: TSCH: Frame-Based and ACK-Based Synchronisation
TSCH uses implicit synchronisation with a neighbour on each frame transmissions
The receiver calculates the difference between the expected and actual time of frame arrival
In frame-based synchronisation, the receiver uses this offset to synchronise to the clock of the sender
In ACK-based synchronisation, the receiver adds this offset in the acknowledgement frame and the sender uses it to synchronise to the clock of the receiver
In the absence of data, devices need to exchange an empty Keep-Alive frame to re-synchronise
  Significant overhead in applications that transmit very infrequently, e.g. smart metering
Tx Data
Tx ACK
Rx ACK
Rx Data
G
G
TxOffset
Timeslot Length
Tx

## Slide 21: TSCH: Absolute Slot Number
A number that counts slots since the formation of the network
  5 bytes so that it can increment for hundreds of years without wrapping
ASN Synchronisation
  ASN is initialised to 0 by the device that forms the network
  Devices learn the current value of ASN when they join the network
  Since they are synchronised, all devices know the current value of ASN at any time

## Slide 22: TSCH: Slot frame and Schedule
Time slots are organised in a slot frame
  A slot frame is a continuously repeating pattern of slots
  Slot frame size (not defined by the standard, tailored to the application)
  [slot offset] = [ASN] % [slot frame size]
Communication is based on a schedule, for example:
  Slot frame size = 7
  B transits to A in slot offset = 1

## Slide 23: TSCH: The Schedule Controls Several Performance Metrics
Assuming timeslot size 10 ms and frame size 7…
Link Capacity: 100 / 7 = 14.28 packets per second
Energy Consumption: 1 / 7 = 14.28% radio duty cycle
Latency: up to 7 x 10 ms = 70 ms

## Slide 24: TSCH: Slot Frame Size
Defines the number of idle slots in a frame
Shorter slot frame size
  More transmission opportunities → higher capacity for data
  More re-transmission opportunities → higher reliability
  Shorter average and worst-case latency
  More unused slots → worse energy-efficiency
  Less room for other devices → worse scalability

## Slide 25: TSCH Schedule: Dedicated Slots
In each slot, a device can transmit (Tx), receive (Rx), or sleep (idle)
Dedicated slots (Contention-free)
  Slot dedicated to a specific link
  One assigned transmitter → no collisions
  Example: B>A, means B transmits (Tx) and A receives (Rx)

## Slide 26: TSCH Schedule: How many slots?
Why did I allocate 2 slots per frame for link C>A?
How many slots per frame I need generally?

## Slide 27: TSCH Schedule: How many slots?
Slots in the schedule should be able to have capacity for:
  Packet generation rate by the transmitter
  Packet forwarding rate by the transmitter
  Retransmissions (ETX, Expected Transmission Count)
    ETX = 1/p where p is packet reception probability
    Example: if p=20%, I need to retransmit each packet 5 times on average

## Slide 28: TSCH Schedule: Broadcast Slots
Broadcast slots (every node active)
  If I have something to broadcast, I transmit
  If I have nothing to broadcast, I listen/receive
  Typically, the first slot of the frame
  Collisions may happen
  Transmitters cannot receive broadcasts of others

## Slide 29: Slots Are Limited
Assuming a time slot of 10 ms, there are only 100 slots per second
  Permit for maximum 100 packets per second
What can do if we run out of slots, and we want to support more devices, traffic or retransmissions?

## Slide 30: TSCH Schedule: Shared Slots
Shared slots (Contention-based)
  Slot assigned to multiple transmitters
  Collisions are possible, need CSMA/CA
  Good for devices that transmit sporadically (e.g. event-based)

## Slide 31: TSCH Schedule: Multiple Channels
Parallel transmissions are possible in different channels
  A transmitter and receiver can only tune to one specific channel

## Slide 32: Some Channels are better than others
IEEE 802.15.4 uses retransmissions to combat channel errors
Interference and fading errors are correlated in time
  If a channel experiences a lot of interference now, it is very likely to experience a lot of interference in the next frame
Yet, interference and fading of different channels are often uncorrelated
  If a channel experiences a lot of interference now, it is very likely that another channel will not be affected by the same source of in the next frame
Idea: Change channels for each retransmission to enhance reliability

## Slide 33: TSCH: Channel Hopping
Channels change following a pre-agreed pseudo-random order
All nodes agree on a Channel Hopping Sequence (CHS), e.g. 10-11-12
Channel = CHS[index], where index = ASN mod len(CHS)

## Slide 34: Slot Frame Size vs Channel Hopping Sequence Size
The Slot Frame Size and CHS size must be relatively prime
  Their highest common factor should be 1
Otherwise, there is no channel hopping!
Example: frame size is 6 and CHS size is 3

## Slide 35: The TSCH Schedule
A N-by-M table where N is the slot frame size and M is the CHS size
  Each column represents a slot offset (SO)
  Each row represents a channel offset (CHO)
Channel = CHS[index], where index = (ASN + CHO) mod len(CHS)
CHO \ SO | 0 | 1 | 2 | 3 | 4 | 5 | 6
0 | BC |  | C > A | C > A | B > A |  | 
1 |  |  |  |  | D > C |  | 
2 |  |  |  |  |  |  | 

## Slide 36: TSCH Schedule
Channel = CHS[index], where index = (ASN + CHO) mod len(CHS)

## Slide 37: Channel Selection
Consider a channel with a lot of interference
  Using as the only single channel is very bad
  Using it as part of the CHS is better, but inefficient
How can we select which channels to use?
  Some channels are busier than others
  The quality of the channels changes over time
Adaptive Channel Selection
  Measure the quality of channels
  Update metrics with statistics
  Select the best channels (blacklist/whitelist)
  Distribute changes to the channel hopping sequence
Adaptive Channel Selection: https://doi.org/10.1109/GIOTS.2017.8016246

## Slide 38: TSCH Scheduler
A TSCH Scheduler is an algorithm that determines the TSCH schedule
The Scheduler is not defined by the standard (flexible)
Schedules are tailored to the use case
Types of TSCH Scheduling
  Static Scheduling
  Dynamic Scheduling
    Centralised Scheduling
    Distributed Scheduling
    Autonomous Scheduling

## Slide 39: Static Scheduling
Schedule is hardcoded on the firmware of the devices
A static schedule can be handcrafted or algorithmically derived
Makes sense only in relatively static TSCH networks
  No. of devices, topology, traffic patterns, expected retransmissions
CHO \ SO | 0 | 1 | 2 | 3 | 4 | 5 | 6
0 | BC |  | C > A | C > A | B > A |  | 
1 |  |  |  |  | D > C |  | 
2 |  |  |  |  |  |  | 

## Slide 40: Dynamic Scheduling
A minimal schedule with shared slots is defined
  Hardcoded or installed when joining the network
Dedicated slots are allocated dynamically
Centralised Scheduling
  The root node collects information about the nodes via these shared slots
  Having the global picture of the network, it allocates dedicated slots to specific links
  Such decisions can be determined using machine learning or reinforcement learning
Distributed Scheduling
  Neighbouring nodes exchange information and agree on which slots to use between them

## Slide 41: IETF Minimal Schedule and 6top
Minimal Schedule
  One broadcast slot in offset (0,0)
  The slot frame size and channel sequence size is undetermined
  Hardcoded or installed when joining the network
6top (6TiSCH Operation Sublayer Protocol)
  A protocol to exchange messages for distributed scheduling
CHO \ SO | 0 | 1 | 2 | 3 | 4 | 5 | …
0 | BC |  |  |  |  |  | 
1 |  |  |  |  |  |  | 
… |  |  |  |  |  |  | 
6TiSCH and 6top: https://doi.org/10.1109/COMST.2019.2939407
Command | Code | Description
ADD | 1 | Add slot between two neighbours
DELETE | 2 | Delete slot from schedule
RELOCATE | 3 | Relocate slot in schedule
COUNT | 4 | Count slots
LIST | 5 | List slots
SIGNAL | 6 | Send command
CLEAR | 7 | Clear slots between two neighbours
6top Commands

## Slide 42: Autonomous Scheduling
Each node derives and changes its schedule autonomously
  No need to exchange messages
  Cannot guarantee a collision-free schedule
Shared slots are used for the routing protocol to determine parent nodes
  Nodes autonomously determine when to transmit/receive using routing information
  Devices hash the Node ID or MAC address (of sender or receiver) modulo frame size to determine which slot to use
Orchestra is a widely used autonomous scheduler (albeit not a standard)
Orchestra: https://doi.org/10.1145/2809695.2809714

## Slide 43: Joining a TSCH Network
How does a new device join a TSCH network?
A new device that wants to join a TSCH network:
  Does not know the schedule (unless static scheduling is used)
  Does not know the current ASN
  Does not know when the beginning of a frame/slot is (not in sync)
Enhanced Beacon (EB)
  Devices of the TSCH network periodically broadcast an EB to advertise the network
  EB includes the current ASN and (part of) the schedule
The joining device scans the wireless medium for an EB but without knowing the time and channel of the transmission

## Slide 44: Searching for an EB packet
The joining node scans sequentially all the channels until it receives an EB
  If the CHS is fixed, the joining node needs to search only those channels
  Otherwise, it needs to search all 16 channels
Upon the reception of the first EB, the joining node keeps scanning for a potentially better parent until a timeout or a maximum number of candidate parents is reached
The joining process is notoriously slow and inefficient
  But often considered insignificant in static TSCH networks as it ideally happens just once

## Slide 45: Summary
IEEE 802.15.4 TSCH (Time-Slotted Channel Hopping)
  A reliable wireless solution for the Industry 4.0
TSCH Mechanics
  Efficient time synchronisation
  Reliable communication based on a schedule
  Interference avoidance with channel hopping
  Centralised/Distributed/Autonomous scheduling
  Joining a TSCH network